## Slide 1
ML REVIEW 1 · SRM INSTITUTE OF SCIENCE AND TECHNOLOGY · GROUP AD1
Explainable Multimodal Physics-Aware Deep Learning for EV Battery
Estimating State of Health from ten minutes of voltage, current and temperature - with robust linear regression
Team
Swastik Mukherjee - RA2411026010181
Prahladh Alarpati - RA2411026010171
Aayan Noori - RA2411026010165
B.Tech CSE · Department of Computational Intelligence · October 2026
IN
10 min of V, I and T
from one discharge
MODEL
15 physics features ->
robust linear fit
OUT
State of Health,
with a reason attached
636 cycles · 4 cells · MAE 1.14 pp on an unseen cell

## Slide 2
Problem and Objective
Why State of Health is hard
• An EV battery's real capacity is only known by fully discharging it - which no car can do on the road
• Battery Management Systems must instead infer it from short, noisy sensor windows
• Deep models can do this but give no reason, and nobody certifies a black box for a safety system
• Capacity labels themselves come from coulomb counters that drift and glitch
Capacity fade of the four NASA cells used in this project
UNIT 1
Statistical analysis of a 15,064-cycle battery ageing dataset
UNIT 2
Robust linear regression on physics-aware multimodal features
GOAL
An SOH estimate that is accurate, explainable and fault-tolerant

## Slide 3
Two Datasets, Two Jobs
169,766
raw sensor samples (NASA)
636
discharge cycles, 4 cells
15,064
cycles, 14 cells (HNEI)
15 + 8
engineered and measured features
Dataset A - NASA PCoE
• 4 cells (B0005/6/7/18) cycled to failure at 24 degC
• Within-cycle traces: voltage, current, temperature
• Used for the MODEL - label is measured capacity
• Split by cell: train on 3, test on the 4th
Dataset B - HNEI 18650
• 14 NMC-LCO cells, 8 cycle-summary measurements
• Cell identity had to be rebuilt from cycle-index resets
• Used for the STATISTICS - label is remaining useful life
• Deliberately a different lab, chemistry and format
The leakage trap we had to design around
Full discharge duration correlates 0.997 with the capacity label - because the label IS that duration, integrated. Using it would score a fake R2 of 1.0, so every feature here is capped at the first 600 s.

## Slide 4
Unit 1: Nothing in This Data Is Normal
Normal Q-Q plots - every variable leaves the line at the tails
The four most skewed columns, raw (blue) vs log-transformed (orange)
9 of 9
variables reject normality (D'Agostino and Shapiro, p < 0.001)
0
of them are rescued by a log transform
1.8%
median share of cycles flagged as IQR outliers

## Slide 5
Unit 1: Outliers Hide the Strongest Signal
Same eight columns, two definitions of correlation
What the gap means
• 'Discharge time' scores Pearson r = +0.01 (p = 0.14, not significant)
• The same pair scores Spearman rho = +0.96 - near-perfect
• A handful of cycles logged for days flatten the straight-line fit
• Anyone reporting only Pearson r would discard the best feature in the dataset
0.96
Spearman rho, strongest monotone signal
0.01
Pearson r on the very same pair
8 of 8
features still significant after Holm-Bonferroni

## Slide 6
Unit 1: Structure, Groups and Hypothesis Tests
PCA on rank-transformed features, and the cycles in PC1-PC2 space
Six formal tests
• H1 cells differ in voltage level - Kruskal-Wallis, reject
• H2 variances differ across cells - Levene, reject
• H3/H4 early vs late life - Mann-Whitney, reject (CLES 0.98)
• H5 fade within one cell - Spearman rho = -0.96, reject
• H6 cells differ in RUL - cannot reject, and that is correct
91%
of all variance sits in PC1 alone - one latent ageing axis
5 of 6
hypotheses reject H0 at alpha = 0.05
98.2%
chance a random early cycle outranks a late one
Conclusion that drives Unit 2: non-Gaussian, outlier-heavy, one dominant latent axis, and cells that differ from each other -> a ROBUST LINEAR fit validated by holding out whole cells.

## Slide 7
Unit 2: Multimodal Physics-Aware Features
One cell, three sensors, fresh cycle vs end of life. Shaded band = the only 600 s we allow the model to see.
ELECTRICAL (8)
Internal resistance from the first loaded sample · voltage at 60 / 300 / 600 s · plateau slope · 3.9->3.8 V crossing time · energy and RMS current in the window
THERMAL (4)
Temperature rise · temperature at 600 s · heating rate · thermal dose above ambient (K·h)
PHYSICS COUPLINGS (3)
Joule heat I²Rt · Arrhenius rate factor exp(-Ea/RT) for SEI growth · degrees of heating per Wh delivered

## Slide 8
Unit 2: Five Lines, Five Definitions of 'Fit'
Setup
• Target: SOH = measured capacity / 2.00 Ah rated
• 504 training cycles (B0005/6/7), 132 test cycles (B0018, never seen)
• All 15 features standardised inside the pipeline, so coefficients are comparable
• OLS squares the error - one bad point bends the whole line
• Huber squares small errors, switches to absolute past 1.35 sigma
• RANSAC fits random subsets and keeps the consensus fit
• Theil-Sen takes the median of pairwise slopes
• Quantile regression fits the conditional median
Mean absolute error on the held-out cell, in SOH percentage points
1.14 pp
Huber MAE on an unseen cell
7.0 pp
predict-the-mean baseline
0.953
R² on the held-out cell

## Slide 9
Results on a Cell the Model Has Never Seen
Cell B0018: measured ageing curve vs the curve predicted from 10-minute windows
Predicted vs measured, with the +/- 2 pp band
77%
of test cycles land within 2 percentage points
6.2x
better than the predict-the-mean baseline
3.7 pp
best leave-one-cell-out CV (Theil-Sen)
10.0 pp
same CV for OLS - robust fits transfer better

## Slide 10
The Experiment That Justifies 'Robust'
Test error on clean data as a growing share of TRAINING labels is corrupted
How the test works
• Replace p% of training capacity labels with sensor-fault values: half stuck low at 35% SOH, half spiking to 160%
• The test set stays clean, so any loss is the model being fooled
• OLS peaks at an error of 31 pp - it is predicting nonsense
• Theil-Sen is the instructive failure: its breakdown point is ~29% and it collapses right on cue
• Huber, Quantile and RANSAC never move
29x
worse: OLS at its worst contamination level
1.1x
worse: Huber at its worst
1.29 pp
Huber's worst-case error, still under 1.3 pp

## Slide 11
Explainability: Every Prediction Has a Reason
Effect on SOH per standard deviation, with 95% bootstrap intervals
One cycle decomposed: intercept plus a named contribution per feature
8 of 15
coefficients keep their sign in 95% of bootstrap resamples
20 pairs
of features correlate above 0.9 - credit is shared, so read them as groups
0.3 pp
gap between true and predicted SOH on the worked example

## Slide 12
Conclusion
1
Ten minutes of voltage, current and temperature is enough to estimate State of Health to 1.14 pp on a cell the model never saw.
2
Robustness is not a detail: with 20% faulty labels OLS degrades 29x while Huber stays within 1.1x.
3
Physics-aware features keep the model readable - internal resistance, plateau voltage and temperature rise carry the signal, with intervals.
4
The statistics decided the modelling: non-Gaussian, outlier-heavy data with cell-to-cell differences demands a robust fit and grouped validation.
Limitations
Only 4 cells, one ambient temperature (24 degC) · constant-current discharge only, not a real drive cycle · 20 correlated feature pairs blur individual coefficients · single held-out cell
Future Work
More cells and varied temperatures · physics-informed neural network with the same features as inputs · per-cell random effects · online recursive update inside a live BMS